| Company Name | STN Atlas Marine Electronics | STN Atlas Marine Electronics | STN Atlas Marine Electronics | STN Atlas Marine Electronics | STN Atlas Marine Electronics | Tamaya Technics | Tritech |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Name of Product | ATLAS DESO 14 | ATLAS DESO 25 | ATLAS DESO 17 | ATLAS DESO 300 | ATLAS DESO 30 | Tamaya Echo-Sounder TDM 9000 | PA 200 |
| Year of first Manufacture | 1995 | 1990 | 1998 | 1999 | 2001 | 10 years | 1996 |
| Supply Voltage [Volts] | 18-32 VDC | 24 VDC | 115/230 VAC or 18-32 | 11-28VDC standard, 115/230 VAC optional | 115/230 VAC or 18-32 VDC | 12 VDC | 12 VDC or 24 VDC |
| Maximum Power consumption [Watts] | 50 | 150 | 100 | 50 | 75 | 10 | 2 |
| System weight in air [kg] | 7 | 26 | 18 | 145 | 21 | 7,5 | 1,1 |
| Dimensions (width (or diam.) x height x depth) [mm] | 245 x 340 x 215 | 440 x 488 x 270 | 485 x 312 x 335 | 425 x 356 x 203 | 443 x 444 x 275 | 363 x 256 x 120 | N/A |
| installation Options | Portable | 19 inch rack mounted, Bulkhead/ wall mounted, Stand-alone unit | 19 inch rack mounted, Stand-alone unit | 19 inch rack mounted, Bulkhead/ wall mounted, Portable, Water-proofed/Splashproof, Stand-alone unit | 19 inch rack mounted, Bulkhead/wall mounted. Waterproofed/ Splashproof, Stand-alone unit | Portable Stand-alone unit | Portable |
| Depth ranges [mtrs] | 0,5-650 | 0,2- 15000 | 0,2-1800 | 0,2-300 | 0,10-5000 | 0,7-100 | 1-10 or 0,5-50 |
| Frequency Ranges [kHz] | 28-225 | 12-600 | 15-225 | 33-210 | 12-700 | 200 |  |
| Standard frequencies [kHz] | 33,210 | 12,15,33,210 | 33,210 | 210,200,40,33 | Tuneable | 200 | 200 |
| No of frequencies supported simultaneously | 1 | 2 (optionally selectable out of 3) | 2 (optionally selectable out of 3) | 1 | 2 |  | 1 |
| Transducer power @ standard freq. [Watts @ kHz] | 660,300 | 2000,4000,600,300 | 1000,600,300 | 35-600 selectable | 500 @ 210 kHz, 2000 @ 12 kHz | 20 | 190 decibels re micropascals at Im |
| Transducer installation options | Hull mounted. Portable | Hull mounted. Portable | Hull mounted, Portable | Hull mounted, Portable | Hull mounted, Portable | Portable | Portable, ROV/AUV |
| Transducer material | Piezo-Ceramics, Polyurethane, Urethane/Bronze, Barium titanate/Lead Zirconare titanate | Piezo-Ceramics, Polyurethane, Urethane/Bronze, Barium titanate/Lead Zirconate titanate | Piezo-Ceramics, Polyurethane, Urethane/Bronze, Barium titanate/Lead Zirconate titanate | Piezo-Ceramics, Polyurethane, Urethane/Bronze, Barium titanate/Lead Zirconate titanate | Piezo-Ceramics, Potyurethane, Urethane/Bronze, Barium titanate/Lead Zirconate titanate | Barium titanace/Lead Zirconace titanate | Polyurethane Barium titanate/Lead Zirconate titanate |
| Compatible 3rd party Transducers | Any | Any | Any | Any | Any |  |  |
| Along Track beam angle [degrees @ kHz] | 2,4/9 @ 210, 10/18 @ 33 | 24/9 @ 210, 4/10/18 @ 33, 24/46 @ 15 switchable, 15 @ 12 | 2,4/9 @ 210, 10/18 @ 33, 24/46 @ 15 switchable | 2,4/9 @ 210(200), 10/18 @ 33 | Any | 6 @ 200 | 20 @ 200 |
| Across Track beam angle [degrees @ kHz] | 2,4/9 @ 210, 10/18 @ 33 | 24/9 @ 210,4/10/18 @ 33 24/46 @ 15 switchable, 15 @ 12 | 2,4/9 @ 210, 10/18 @ 33, 24/46 @ 15 switchable | 2 4/9 @ 210(200), 10/18 @ 33 | Any | 6 @ 200 | 20 @ 20 |
| Depth Resolution (R), Accuracy (A) and Range (RA) [mtrs, mtrs, mtrs] | R=0,01 А=0,02 RА=10 | R=0,01 A=0,02 RA= 10 | R=0,01 А=0,02 RA=10 | R=0,01 A=0,02 RA=10 | R=0,01 A=0,02 RA=10 | A=0,03 + 0,1% of RA | 0,001 |
| Minimum & Maximum Pulse lengths [milliseconds] | 0,04-0,4 | 0,04-18 | 0,04-0,8 | 0,04-0,4 auto pulse length | 0,01-12,8 | 100-200 | 0,1 |
| Maximum Pulse/ Sounding rate [Hz] | 20 | 40 | 20 | 15 | 25 | 6 | 10 |
| Capable of being operated remotely (e.g. via PC) | Yes | Yes | Yes | Yes | Yes | No | Yes |
| External Data inputs supported | All | All | All | All | All | Event marker |  |
| Depth trace annotation options | internal generated, external generated, programmable | Internal generated external generated, programmable | Internal generated, external generated, programmable | Internal generated, external generated, programmable | Internal generated, External generated, programmable | No |  |
| Depth display information options | Paper trace, digital LCD display | Paper trace digital LCD display | Paper trace digital LCD display | Paper trace, digital LCD display | Paper trace, digital LCD display, Option colour LCD display | Paper trace, digital LCD display by RS-232C to PC |  |
| Recording medium options | Paper recording. External recording to PC | Paper recording. External recording to PC | Paper recording. External recording to PC | Paper recording, External recording to PC | Raw depth data for all frequencies, Raw heave/Pitch/Roll data, NMEA compatible heave corrected depth for all frequencies, Trigger external alarm, Transmission of data to slave unit. | Paper recording External recording to PC External recording to Data Collector | Raw depth data for all frequencies |
| Data output options | Raw depth data for all frequencies, Raw heave/Pitch/Roll data, NMEA compatible heave corrected depth for all frequencies, Trigger external alarm, Transmission of data to slave unit. | Raw depth data for all frequencies Raw heave/Pitch/Roll data, NMEA compatible heave corrected depth for all frequencies, Trigger external alarm, Transmission of data to slave unit. | Raw depth data for all frequencies, Raw heave/Pitch/Roll data, NMEA compatible heave corrected depth for all frequencies, Trigger external alarm, Transmission of data to slave unit. | Raw depth data for all frequencies, Raw heave/Pitch/Roll data, NMEA compatible heave corrected depth for all frequencies, Trigger external alarm, Transmission of data to slave unit. | Raw depth data for all frequencies. | Raw depth data for all frequencies. | Raw depth data for all frequencies. |